Extended Euclidean Algorithm (EEA)
Polynomial Inversion over GF(2m)
Based on
Extended Euclidean Algorithm (EEA)
FPFG Design and Implementation
Presented by: Ibrahim Hazmi
Supervisor: Dr. Fayez Gebali

---
Objective
- Design a Digital Circuit that computes the Modular Inverse of Polynomial function over Binary Field.
- The Polynomial binary field Inverter is based on Extended Euclidean Algorithm (EEA) .
- The design entry method is VHDL and the target implementation platform is Xilinx Spartan3E FPGA.

---
Overview
Based on the following algorithm, the design is simply an Extended GCD data-path unit and FSM controller
BDA: Binary Division Algorithm
1. a←ax, f← fx .
2. g1←0, g2←1.
3. While r≠0 (gcd ≠1) do
   3.1 perform BDA to find r & q (f=a*q+r).
   3.2	g1←g2, g2←g1  qg2.
4. Return(g2).
INPUT: Binary polynomials a(x) of max degree m−1 & f(x) of m degree
OUTPUT: a−1 mod f.
Irreducible Poly
Control
Signals Input
EEA Data-path
EEA
FSM
Controller

---
The Top Level and the Extension Modules
Inverse Extension
r = f - a * quotient
1
a-1
0
a(x)
f(x)
MUX_a
1 0
f
MUX_f
1 0
a
Reg_a
r=0
GCD
Binary Division Algorithm
f = a * quotient + r
Remainder Quotient
Reg_f
Reg_r
Reg_q
r
q
XOR
g1 ⊕ q*g2
MUL
q*g2
MUX_g2
0 1
Reg_g2
Reg_g1
1
a-1
q
g2_xor
g2_mux
g1_mux
g2
g1
MUX_g1
0 1
0
g1_mux
g2_mul

---
The BDA Module and Algorithm
1. a←ax, f← fx .
2. r←0, q←1.
3. WHILE f_deg>a_deg DO
   3.1 dfa←f_deg - a_deg.
   3.2 a←a <<dfa.
   3.3 r←a xor f.
   3.4 dfr←f_deg – r_deg.
   3.5 IF r_deg>a_deg THEN
   q←(q<<dfr) + 1.
   3.6 ELSE
   q←q<<dfa.
4. Return(r, q).
INPUT: a(x) & f(x)
OUTPUT: r and q.

---
FSM Controller
___
Start
S0
Input fx, ax
En_a
En_Ext
S1
Sel_f
Sel_Ext
Start
S2
Sel_a
Sel_Ext
S3
Done
__ ___ ______
r0 . (dfr0 + a_deg0)
 __ __
fgea + dfr0
__ ___ ______
r0 . (dfr0 + a_deg0)
En_a, En_Ext

---
Design Requirements:
- The main focus in the design was on the Functionality
- 3 Registers for the Extention circuit
- 3 Registers for the BDA circuit
- 1 Multiplier and 1 XOR for the Extention circuit
- 2 Subtractors (SADs), 3 Barrel Shifters, 1 XOR, and 3 CLZ circuits for the BDA circuit
  - SAD: Sum of Absolute Diffrence Circuit